## Slide 1: Smart Living Lab at UoWM
Student Dormitories Building – Kozani

## Slide 2: Building Characteristics
Structured area: 4212 m2
Ceiling / floor surface: 2430 m2
Floors: 1 or 2, depending on the space
Openings: 800 m2
The entity has 190 single rooms
The building has undergone insulation improvement, including the addition of insulation for the major part of the roof and walls, while the openings are double glazed ones.
Heating is provided by an oil boiler / conventional terminal units (radiator ones), while the same applies to the Domestic Hot Water (central boiler of the campus).
Cooling units are not present.
Fluorescent lamps are used.

## Slide 3: History
Developed, expanded and certified under various projects, starting at 2017
PV-Estia
MOST
3. Berlin
4. Regional Excellence

## Slide 4: History and Rationale
Developed and expanded under various projects, starting at 2017
Aim to use the building of the dormitories as a “living lab”, where real people live in and interact
Target, to create a “user friendly” environment for testing industry products and for research purposes

## Slide 5: Photovoltaics and battery systems
35.4 kWp of PV
31.4 kWh of battery systems (Li-Ion)
Divided in three subsystems
Using three hybrid inverters

## Slide 6: Energy meters
Power quality analyzers monitoring multiple points of the installation (including up to 50th harmonic)
Thermal energy meter

## Slide 7: Weather station and other meters
Meteorological station
Thermometers and humidity meters
  At corridors
  At certain rooms

## Slide 8: Car charger
22 kW AC charger
Capable of 2 simultaneous charging processes

## Slide 9: Energy management system
Siemens controller for regulating
  car charger
  battery
  shiftable loads
  3 electronically programmable loads (by Chroma)

## Slide 10: Extra features
Smart plugs at certain rooms for
  switch control capability
  energy monitoring
Corridor lighting switchboard ready for the control through remote switch capability

## Slide 11: Measurements database
For the collection of all measurement data
For downloading requested datasets
For visualization of measurements
For monitoring the integrity of collected measurements
With e-mail notification with the status of collection system
With e-mail notification in case of measurement device disconnection

## Slide 12: Electrical diagram

## Slide 13: Research Activities
PV and load forecasting models
Non-Intrusive Load Monitoring (NILM) algorithms
Open Access database
EV optimal charging schemes